Daniel MacMillan
Dangnhi Ngo
Lab 3

Individual Questions – Daniel

1) Our lab 2 robot was a Braitenberg Vehicle in the sense that it had two sensors that controlled two motors that would steer the robot in reaction to some stimulus – in this case the color of the ground beneath the sensor.

2) Braitenberg's method can be used to describe complex robot behaviors because even with just two motors and two sensors, behavior can be changed according to how one programs the robot to react to the sensor readings. One can program the robot to slow down after

Also, different sensors can be added on to the robot, as well as different types of outside stimulus that can trigger different types of sensors. There is also a way to

Part A

1) Light sensor readings fall below 2000 when a flashlight is shown nearby from a standing value of 3000 with just the lights from the room.

2) The light sensor readings vary by a factor of 200 when shone under the same light. They both prefer the light source to be straight ahead of them, and not above or to the side of them.

3) The minimum readings we can obtain is under 200, the maximum reading we can obtain is just under 4000, the typical readings in a lit room is around 3500.

4) One of our light sensors is slightly stronger than the other, its readings vary from the other by a factor of 200.

/* Daniel MacMillan and Dangnhi Ngo
 *
 * Lab 3 - Part A
 * Print out the sensor readings from the analog ports.
 */

#include <kipr/botball.h>

int main()
{
while(!c_button_clicked())
    {
    printf("%d %d\n", analog(0), analog(1));
    }
    return 0;
}

Part B

For both sensors, the readings when the light is pointed directly down the tubes is under 200. When the sensor turns away at 10 degrees, the value goes up slightly up to 1000. When the sensor turns away from the light at 20 degrees, the sensor readings go back up to 3000, and completely lose any indication that the light is there at all beyond that angle.

Part C

/* Daniel MacMillan and Dangnhi Ngo
 *
 * Lab 3 - Part C
 * normalize light readings to motor commands
 */

#include <kipr/botball.h>

#define MAX_VEL 25

/* Normalize: take light reading from individual sensors and turn it into
 * the proper motor speed.
 */
int normalize(int light)
{
    int MAX_LIGHT = 100;
    int MIN_LIGHT = 4000;

    int output = ((light - MIN_LIGHT) * 100) / (MAX_LIGHT - MIN_LIGHT);

    // correct the values if they somehow go overboard
    if(output < 0)
        return 0;
    if(output > 100)
        return 100;
    return output;
}

Part D - FOLLOW

The light seeking algorithm we have written works to try and turn the robot, but next time we should change the hardware of the robot to make it physically turn the robot around.

/* Daniel MacMillan and Dangnhi Ngo
 *
 * Lab 3 - Part D
 * normalize light readings to motor commands and make it follow light
 */

#include <kipr/botball.h>

#define MAX_VEL 25

/* Normalize: take light reading from individual sensors and turn it into
 * the proper motor speed.
 */
int normalize(int light)
{
    int MAX_LIGHT = 100;
    int MIN_LIGHT = 4000;

    int output = ((light - MIN_LIGHT) * 100) / (MAX_LIGHT - MIN_LIGHT);

    // correct the values if they somehow go overboard
    if(output < 0)
        return 0;
    if(output > 100)
        return 100;
    return output;
}

int main()
{
    while(!c_button_clicked())
    {
        // print the new motor values
        int normal_left = normalize(analog(0));
        int normal_right = normalize(analog(1));
        printf("Left: %d | Right: %d\n", normal_left, normal_right);

        // move the motors based on light values
        // if we want to avoid light, make motor values negative, or	swap normal_left/right
        motor(0, normal_right);
        motor(1, normal_left);
    }
    ao();
    return 0;
}

Part D – AVOID

The way our robot avoids light is by swerving to the right when the right sensor detects light, and swerves left when the left sensor detects light. All that we did to accomplish this was swapping normalized values going to the motors from the avoid program.

#include <kipr/botball.h>

#define MAX_VEL 25

/* Normalize: take light reading from individual sensors and turn it into
 * the proper motor speed.
 */
int normalize(int light)
{
    int MAX_LIGHT = 100;
    int MIN_LIGHT = 4000;

    int output = ((light - MIN_LIGHT) * 100) / (MAX_LIGHT - MIN_LIGHT);

    // correct the values if they somehow go overboard
    if(output < 0)
        return 0;
    if(output > 100)
        return 100;
    return output;
}

int main()
{
    while(!c_button_clicked())
    {
        // print the new motor values
        int normal_left = normalize(analog(0));
        int normal_right = normalize(analog(1));
        printf("Left: %d | Right: %d\n", normal_left, normal_right);

        // move the motors based on light values
        // if we want to avoid light, make motor values negative, or	swap normal_left/right
        motor(0, normal_left);
        motor(1, normal_right);
    }
    ao();
    return 0;
}

Part E
The bumper code does the trick when trying to avoid obstacles because without it, the robot could keep moving toward light when it bumps into the light. The light sensor has no way of detecting how close a light source actually is, so this is a welcome addition.

/* Daniel MacMillan and Dangnhi Ngo
 *
 * Lab 3 - Part E
 * add bumper code from lab 1 so that the robot avoids obstacles
 */

#include <kipr/botball.h>

#define MAX_VEL 25

/* Normalize: take light reading from individual sensors and turn it into
 * the proper motor speed.
 */
int normalize(int light)
{
    int MAX_LIGHT = 100;
    int MIN_LIGHT = 4000;

    int output = ((light - MIN_LIGHT) * 100) / (MAX_LIGHT - MIN_LIGHT);

    // correct the values if they somehow go overboard
    if(output < 0)
        return 0;
    if(output > 100)
        return 100;
    return output;
}

/* turn_around: procedure from lab 2 to be called when the bumper is hit.
 */
void turn_around()
{
// first go backward
    motor(0,-MAX_VEL*2);
    motor(1,-MAX_VEL*2);
 msleep(700);
    // then swivel around to go a different direction
    motor(0,-MAX_VEL*2);
    motor(1, MAX_VEL*2);
    msleep(2000);

    return;
}

int main()
{
    while(!c_button_clicked())
    {
        // print the new motor values
        int normal_left = normalize(analog(0));
        int normal_right = normalize(analog(1));
        printf("Left: %d | Right: %d\n", normal_left, normal_right);

        // move the motors based on light values
        // if we want to avoid light, make motor values negative
        motor(0, normal_right);
        motor(1, normal_left);

        // Hit detection
        if(digital(2) || digital(3))
        {
        turn_around();
        }

        msleep(20);
    }
    ao();
    return 0;
}